## Slide 1: You Are the Emergency Medical Responder
A 45-year-old man is experiencing chest pain. When help arrives you learn that the onset of pain started about 30 minutes ago as a mild, squeezing sensation. The pain is now severe and he is gasping for breath. You, as the responding member of your company’s emergency response team, recognize that these signs and symptoms suggest a serious cardiac condition. You complete a primary assessment, physical exam and SAMPLE history. The patient has no known history of hypertension or heart disease. While waiting for an ambulance to arrive, you help the patient get into the most comfortable position for breathing, keep him from getting chilled or overheated and ask him to remain still. You open a nearby window to circulate fresh air into the stuffy room.
Lesson 16: Emergency Oxygen
Notes: <number>

## Slide 2: Indications for the Use of Emergency Oxygen
For a nonbreathing patient having a breathing emergency
The use of oxygen in breathing adults, children and infants depends on the number of breaths per minute
  Adult: >12 or <20 breaths per minute
  Children: >15 or <30 breaths per minute
  Infants: >25 or <50 breaths per minute
For suspected CO poisoning and all smoke inhalation cases

## Slide 3: Emergency Oxygen Components
Oxygen cylinder
Pressure regulator
and flowmeter
Delivery device

## Slide 4: Types of Oxygen Delivery Systems
Variable-flow-rate oxygen systems
  Able to adjust flow rate
  Require equipment assembly
Fixed-flow-rate oxygen systems
  Set flow rate, usually 15 LPM
  No assembly required

## Slide 5: Oxygen Delivery Devices
Nasal cannula
Resuscitation mask
Non-rebreather mask
BVM

## Slide 6: Nasal Cannula
For use only on breathing patients, delivering emergency oxygen through the patient’s nostrils
Commonly used for patients with only minor breathing difficulty or for those who have a history of respiratory medical conditions; also useful for patients who cannot tolerate a mask over their face
Flow rate of 1 to 6 LPM
Peak oxygen concentration of approximately 44 percent

## Slide 7: Resuscitation Mask with Oxygen Inlet
For nonbreathing patient or someone who is breathing but still needs emergency oxygen
Flow rate of 6 to 15 LPM
Peak oxygen concentration of 55 percent at 6 LPM
Peak oxygen concentration of 35 percent when used on a nonbreathing patient during ventilations

## Slide 8: Non-Rebreather Mask
For delivery of high concentrations of oxygen to breathing patients
Face mask with attached reservoir bag and one-way valve
Flow rate at 10 to 15 LPM
Peak oxygen concentration up to 90 percent with a high oxygen flow rate

## Slide 9: BVM
For breathing and nonbreathing patients
Flow rate at 15 LPM or greater
Peak oxygen concentration of 90 percent or more when flow rate at 15 LPM or more

## Slide 10: Activity
While providing care to a patient in a motor-vehicle crash, your assessment reveals that the patient’s respiratory rate is 30 breaths per minute. The patient also has a history of pneumonia. You determine that the patient would benefit from emergency oxygen.

## Slide 11: Safety Precautions
Be sure oxygen is flowing before applying the delivery device.
Do not use oxygen around flames or sparks including smoking materials.
Do not use grease, oil or petroleum products to lubricate or clean the regulator.
Do not stand oxygen cylinders upright unless secured.
Do not drag or roll cylinders.
Do not carry a cylinder by the valve or regulator.
Notes: <number>

## Slide 12: Safety Precautions (cont.)
Do not hold on to protective valve caps or guards when moving or lifting cylinders.
Do not deface, alter or remove any labeling or markings on the oxygen cylinder.
Do not attempt to mix gases in an oxygen cylinder or transfer oxygen from one cylinder to another.
Do not defibrillate someone when around free-flowing oxygen or gasoline.
Never refill an oxygen cylinder.

## Slide 13: You Are the Emergency Medical Responder
The 45-year-old man who was experiencing chest pain and difficulty breathing is now slightly cyanotic (skin has a bluish color), is gasping for air and is breathing 26 times per minute.
After a couple of minutes, the man complains of having a mask on his face but is still gasping for air.